## Slide 1: GroupConvolution on GNA
Some notes by Mike Deisher
November 2022

## Slide 2: OpenVINO Definition
Dimensions
  Input: N,C,H,W
  Kernel: G,Co,Ci,H,W
In the example, 1,8,48,48 * 8,1,1,3,3
  G=8 means split input channels into 8 equal groups of 1 each
G==Ci is DWSC
Notes: https://blog.yani.ai/filter-group-tutorial/

## Slide 3: Piotr Rozen’s 1D DWSC
H=8
C=8
No padding,
stride 2
C=8
K=1x3
Σ
Σ
Σ
H=3
G=8
Elementwise
Multiply per
Kernel element

## Slide 4: Naïve Solution
The main problem: GNA convolution has no strided memory access
Secondary problem: GNA has no strided copy
  Even if it did this solution requires G times more memory bandwidth
Claim: the best we can do to solve the general problem is:
  Large transpose
    Requires >2*2*N*H*W*C additional memory bandwidth
    May not work for all problem sizes
  G individual convolutions
  Concat
    May be VERY costly if parts are not 64B aligned
  Number of layers can be quite large
  If input tensor is not too big and dimensions are “nice” this approach is feasible

## Slide 5: Naïve 1D DWSC
H=8
C=8
No padding,
stride 2
C=8
K=1x3
Transpose,
Split, &
Convolve
H=3
G=8
Pad,
Transpose,
Split

## Slide 6: Naïve Method vs Piotr Rozen’s 1D DWSC
For 1D problems Piotr’s solution is better
  Inefficient but in-place so no extra memory movement
  Does not require unaligned memory operations on convolution output
  66% faster on customer DWSC model on MTL
Drawbacks
  For some problems, it results in many more layers
  Does not work for 2D
  Does not generalize to Group Convolution

## Slide 7: Source Code
https://github.com/intel-sandbox/gna_tools/tree/main/run_ngraph
  See groupconv_decomposition.cpp
  run_ngraph is a command line tool to perform a sequence of transformations on an IR graph producing a new IR graph
https://github.com/intel-sandbox/gna_tools/tree/main/make_ngraph
  make_ngraph is a command line tool to construct simple networks for testing

## Slide 8: Questions?